## Slide 1: Welcome
To
Our Presentation
Session-1

## Slide 2: Thermodynamics & Heat Engine (67061) 6th SEMESTER Mechanical Department
Chapter-1
The Scope and Basic Concept of Thermodynamics
Presented By
Engr. Jannatul Ferdousy
Instructor(Mechanical)
Dhaka Polytechnic Institute

## Slide 3: Learning Outcome(Chapter-1):
What is Thermodynamics?
Applications of Thermodynamics.
Know about Heat and Temperature.
Different Units of Heat.
Relation one heat unit to another heat units.

## Slide 4: Thermodynamics:
Thermodynamics:
Thermodynamics is the branch of science of the relationship between heat, work, temperature, and energy. In broad terms, thermodynamics deals with the transfer of energy from one place to another and from one form to another. The key concept is that heat is a form of energy corresponding to a definite amount of mechanical work.
Applications of Thermodynamics:
Refrigerators, Deep freezers , Industrial refrigeration systems
Air-conditioning systems, Heat pumps
Air and gas compressors,
Blowers, Fans, Run on various thermodynamic cycles etc.

## Slide 5: Heat and Temperature:
Heat:
Heat is the thermal energy transferred from a hotter system to a cooler system that are in contact.
Teamperature:
Temperature is a measure of the average kinetic energy of the atoms or molecules in the system.

## Slide 6: Different Units of Heat:
The most common units of heat are
BTU - British Thermal Unit
Calorie.
Joule.
Calorie:
In CGS Unit, heat is expressed in the unit of calories which is further said to be the heat energy needed to increase the temperature of 1 gm of clean water by 1 temperature.
1 cal = 1 gm clean water × 1 temperature kilocalorie:
One kilocalorie is the amount of heat needed to raise the temperature of 1 kilogram of clean water by 1 temperature.
1 kcal = 1 kg clean water × 1 temperature

## Slide 7: Different Units of Heat:
BTU:
It is defined as the amount of heat required to raise the temperature of one pound of water by one degree Fahrenheit.
1 BTU = 1 lb clean water × 1 temperature
Therm:
It is defined as the amount of heat required to raise the temperature of 1000 pound of water by 100 degree Fahrenheit.
1 Therm = 1000 lb clean water × 100 temperature
CHU:
The centigrade heat unit (CHU) is the amount of heat required to raise the temperature of one pound of water by one degree Celsius.
1 CHU = 1 lb clean water × 1 temperature
Joule:
The standard unit for the rate of heat transferred is the watt (W), defined as one joule per second.
1 cal = 4.1868 4.2 Joule ; 1 kcal = 4200 Joule = 4.2 kJoule

## Slide 8: Relation one heat unit to another heat units:
(1) Relation between BTU & cal :
1 BTU = 1 lb clear water × 1 temperature
= 453.6 gm × [ 1 lb = 453.6 gm & 1 = ]
= 252 cal (Ans.)
Again, Again,
252 cal = 1 BTU 1 cal =4.2 Joule
1 cal = BTU 252 cal = 4.2 × 252 Joule
= 3.968 × BTU (Ans.) = 1058.4 Joule (Ans.)
(2) Relation between CHU & Cal ; Relation between BTU & CHU …..etc.

## Slide 9: Chapter-2
Specific Heat of Gases

## Slide 10: Learning Outcome(Chapter-2):
What is Specific Heat , Thermal Capacity , Water Equivalent?
Know about Specific Heat at constant volume ( ).
Know about Specific Heat at constant pressure( ).
Relation between Specific Heats( & ).

## Slide 11: Specific Heat , Thermal Capacity and Water Equivalent :
Specific Heat:
The specific heat is the amount of heat per unit mass required to raise the temperature by one degree Celsius.
Specific Heat ,S = (Here, H= Heat , m= mass , t= temperature)
Unit of Specific Heat cal/gm, kcal/kg ,BTU/lb , Joule/ kg.k.
The specific heat of water is 1 cal/ gm°C
= 1 kcal/kg
= 4200 Joule/ kg.k
= 4.2 KJ/ kg.k

## Slide 12
Thermal Capacity:
Thermal capacity is the property of a material to absorb heat when it is heated and to release heat when it is cooled . The heat required to raise the temperature by one degree Celsius.
Thermal Capacity , C = ms cal
Thermal Capacity = mass × Specific Heat
Unit of Thermal Capacity is cal , kcal , BTU , Joule .

## Slide 13
Water equivalent:
To heat a liquid it is necessary to provide a container and in the process of applying heat the container will absorb some of the heat supplied.
“The water equivalent of a body is the mass of water which would take up as much heat as the body when the temperature rise was the same for each.”
Water equivalent = mass of body × specific heat.
W = ms gm
Unit of Water equivalent is gm ,kg , lb .

## Slide 14: Specific Heat at constant volume ( ):
Specific heat at constant volume represents the heat supplied to a unit mass of the system to raise its temperature through 1, keeping the volume constant. The specific heat at constant volume is Cv .
Let , m kg gas at constant volume is heated at to temperature.
Let, m = mass of gas
= Initial Temperature
= Final Temperature
H = Heat Flow
At constant volume Heat flow ,H=m( - )
Since there is no change of volume, no work done is happened in this process . That’s why W=0 and at constant volume Internal energy is equal to Total Heat flow.
of Air is 0.172 cal /gm or 0.172 kcal/ kg.k or 0.720 kJ/kg.k.

## Slide 15: Specific Heat at constant pressure( ):
Specific heat at constant pressure represents the heat supplied to a unit mass of the system to raise its temperature through 1, keeping the pressure constant. The specific heat at constant pressure is
Let , m kg gas at constant pressure is heated at to temperature.
Let, m = mass of gas
= Initial Temperature
= Final Temperature
H = Heat Flow
We know, at constant pressure, Heat flow, H = m)
Work done ,W= =
And Internal energy , E = m
At constant pressure, heat flow (q) and internal energy (E) are related to the system's enthalpy (H).
The heat flow is equal to the change in the internal energy of the system plus the PV work done.
of Air 0.240 cal/gm or 0.240 kcal/kg.k or 1.005kJ/kg.k.

## Slide 16: Relation between Specific Heats( & ):
Let , m kg gas at constant pressure is heated at to temperature.
Let, m = mass of gas
= Initial Temperature
= Final Temperature
= Initial Volume
= Final Volume
H = Heat Flow
P = Constant Pressure
= Specific heat at constant pressure
= Specific heat at constant volume
We know, at constant pressure, Heat flow, H = m)
Work done ,W= =
And Internal energy , E = m
At constant pressure, heat flow (q) and internal energy (E) are related to the system's enthalpy (H).
The heat flow is equal to the change in the internal energy of the system plus the PV work done.

## Slide 17: Continued…..
The first law of thermodynamics , we know , H=E+W
At constant pressure , H = m +
m) = m +……..(1)
Characteristics equation of a gas We know,
PV =mRT ( Here, R= gas constant)
P= mR ( Initial state)
and P = mR( Final state )
P( - ) = mR( -
Now put the value of P( - ) in equation (1)

## Slide 18: Continued…….
From equation (1)
m) = m +
= +
- = or = R
If = ( -1 ) =

## Slide 19: Chapter-3
Concept of Latent Heat and Sensible Heat

## Slide 20: Learning Outcome(Chapter-3):
What is Sensible heat and Latent Heat ?
Classification of Latent Heat .
How to Calculate Sensible Heat and Latent Heat?
Solved Problem.

## Slide 21: Sensible heat and Latent Heat:
Latent and sensible heat are types of energy released or absorbed in the atmosphere.
Sensible heat:
Sensible heat is related to changes in temperature of a gas or object with no change in phase.
Latent heat:
Latent heat is related to changes in phase between liquids, gases, and solids.

## Slide 22: Sensible Heat and Latent Heat Diagram

## Slide 23: Classification of Latent Heat:
Latent Heat of Fusion( গলনের সুপ্ততাপ )
Latent Heat of Solidification( কঠিনীভবনের সুপ্ততাপ )
Latent Heat of Vaporization( বাষ্পীভবনের সুপ্ততাপ )
Latent Heat of Condensation( ঘনীভবনের সুপ্ততাপ )

## Slide 24
latent heat of fusion:
It is a category of latent heat describing the energy for the phase change between a liquid and a solid to occur without a change in temperature.
Latent heat of solidification:
Heat liberated by a unit mass of liquid at its freezing point when it solidifies. Heat absorbed or radiated during a change of phase at a constant temperature and pressure.
Latent heat of vaporization:
It is a physical property of a substance. It is defined as the heat required to change one mole of liquid at its boiling point under standard atmospheric pressure.
Latent heat of condensation:
It is energy released when water vapor condenses to form liquid droplets. An identical amount of calories (about 600 cal/g) is released in this process as was needed in the evaporation process.

## Slide 25: List of Unit of different Latent Heat:
In CGS Unit, Latent heat of fusion and solidification of ice is 80 Cal /gm .
In MKS Unit, Latent heat of fusion and solidification of ice is 80 kcal/kg.
In SI Unit, Latent heat of fusion and solidification of ice is 335 kJ/kg.
In CGS Unit, Latent heat of vaporization and condensation of water is 539 Cal /gm .
In MKS Unit, Latent heat of vaporization and condensation of water is 539 kCal /kg.
In SI Unit, Latent heat of vaporization and condensation of water is 2257 kJ/kg .

## Slide 26: The formula to calculate the Sensible Heat and Latent Heat:
Let, H = Sensible Heat
m = mass
t = temperature change
s = Specific heat
t = -
Sensible Heat , H = mst Unit: cal, kcal , kJ , BTU, CHU.
Again, Let,
L = Latent Heat
Latent Heat , L = Unit: cal /gm, kcal/kg , kJ/kg ,CHU/lb ,BTU/lb

## Slide 27: Solve Problem:
3.1. -10তাপমাত্রার 5kg বরফকে স্বাভাবিক বায়ুমন্ডলীয় চাপে তাপ প্রয়োগ করে অতিতাপিত স্টিমে পরিবর্তন করা হলো । উৎপাদিত স্টিমের তাপমাত্রা 120হলে সরবরাহকৃত তাপের পরিমাণ কত ? বরফ ও অতিতাপিত স্টিমের আঃ তাপ যথাক্রমে 0.5 এবং 0.48 cal/kg.k , বরফ গলন ও পানির বাষ্পীভবনের সুপ্ততাপ যথাক্রমে 80 ও 538.8 kcal/kg ধর।
Ice Ice Water Water Saturated Steam Superheated Steam
Solution:(1) 5 কেজি বরফকে -10 হতে 0 তাপমাত্রায় আনতে প্রয়োজনীয় তাপ,
= ms( - = 5 0.5 {0 – (-10)} = 25kcal
(2) 0 বরফকে 0 তাপমাত্রার পানিতে পরিণত করতে প্রয়োজনীয় তাপ,
= mL = 5 80 = 400 kcal
-10
0
0
100
100
120

## Slide 28: Continued…….
(3) 0 এর 5 কেজি পানিকে 100 স্ফুটনাঙ্কে তুলতে প্রয়োজনীয় তাপ,
= ms( - = 5 1 (100 - 0) = 500 kcal [ পানির আঃ তাপ1kcal/ kg.k]
(4) 100 তাপমাত্রার বাষ্পকে 100 তাপমাত্রার ভেজা বাষ্পে পরিণত করতে প্রয়োজনীয় তাপ ,
= mL = 5538.8 = 2694 kcal
( 5) 100 এর 5 kg শুষ্ক সম্পৃক্ত স্টিমকে অতিতাপিত করে 120 তাপমাত্রায় তুলতে
প্রয়োজনীয় তাপ ,
= ms( - = 5 0.48 (120 - 100) = 48 kcal
রবরাহকৃত মোট তাপের পরিমাণ ,
H =+ + + +
= 25 + 400 + 500 + 2694 + 48
= 3667 kcal (Ans.)

## Slide 29
3.2. সমান ভরের বরফ ও ফুটন্ত পানি একত্রে মিশ্রিত করা হলো । এতে সম্পূর্ণ বরফ পানিতে পরিণত হলো এবং মিশ্রনের তাপমাত্রা 10। বরফ গলনের সুপ্ততাপ নির্ণয় কর।
Solution: Let, বরফ গলনের সুপ্ততাপ = L cal/gm
বরফ ও ফুটন্ত পানি উভয়ের ভর = m gm
0 তাপমাত্রায় m gm বরফ 0 তাপমাত্রার পানিতে পরিণত হতে গৃহীত তাপ , mL cal
0 তাপমাত্রায় m gm বরফ গলা পানি 10 তাপমাত্রার পানিতে পরিণত হতে গৃহীত তাপ ,
= mst = m× 1 × ( 10 – 0 ) = 10m cal
(3) 100 তাপমাত্রার m gm ফুটন্ত পানি 10 তাপমাত্রায় নামতে বর্জিত তাপ ,
= mst = m ×1 ×(100 – 10) = 90m cal
We know, গৃহীত তাপ = বর্জিত তাপ
+ =
mL + 10m = 90m
L = 80 cal/gm (Ans.)

## Slide 30: Question:(Home Work)(Chapter-1,2,3)
1. থার্মোডাইনামিক্স বলতে কী বুঝায় ?
2. তাপ ও তাপমাত্রার পার্থক্য লেখ ।
3. 1BTU = কত ক্যালোরি ও কত জুল ?
4. একজন অসুস্থ ব্যক্তির দৈহিক তাপমাত্রা ডাক্তারি থার্মোমিটার পাঠে 104 হলে সেলসিয়াস স্কেলে পাঠ কত হবে ?
5. 500 BTU তাপকে তাপের অন্যান্য এককে রূপান্তর কর ।
6. আঃ তাপদ্বয়ের সম্পর্ক হতে প্রমাণ কর যে , - =
7. বরফ গলনের সুপ্ততাপ কাকে বলে ?
8. -20 তাপমাত্রার 30gm বরফ 0 তাপমাত্রার পানিতে রেখে দেখা গেল 3.75gm পানি বরফে পরিণত হলো । যদি বরফের আঃ তাপ 0.5cal/gm হয় , তবে বরফ গলনের সুপ্ততাপ নির্ণয় কর।

## Slide 31
এই ক্লাসের ভিডিও টি পুনরায় দেখতে চাইলে দক্ষতা বাতায়ন (http://skills.gov.bd) ভিজিট করুন ।
THANKS TO ALL