## Slide 1: WELLCOME TO MY PRESENTATION
Presented By
Md. Ashraful Hoque
Junior Instructor (Tech/Mechanical)
Mechanical Technology
Dhaka Polytechnic Institute

## Slide 2: Subject : Thermodynamics And Heat Engine
Topics: Internal Combution Engine (I.C Engine)
Chapter -11

## Slide 3: Internal Combustion Engines
1
Mechanical Engineering Department
Dhaka Polytechnic Institute

## Slide 4: Introduction
Heat Engine:
Heat Engine is a machine which converts heat energy supplied to it into mechanical work.
Heat energy is supplied to the engine by burning the fuel.

## Slide 5: Classification of Heat Engines
Internal Combustion Engines (IC Engines)
In IC engines, combustion of fuel takes place inside the engine cylinder.
Examples: Diesel Engines, Petrol Engines, Gas engines.
External Combustion Engines (EC Engines)
In EC engines, combustion of fuel takes place outside the working cylinder.
Examples: Steam Engines and Steam turbines

## Slide 7: Classification of IC Engines
IC Engines are classified into,
(1) Cycle of operation (No of Strokes per cycle)
•
•
Two Stroke cycle Engines Four Stroke Cycle Engines
(2) Thermodynamic Cycle or Method of Heat addition:
•
•
•
Otto Cycle Engines (Combustion at constant volume) Diesel Cycle Engines (Combustion at constant Pressure) Semi Diesel Engines (Dual Combustion Engines)

## Slide 8: Classification of IC Engines
(3) Types of Fuel Used :
•
•
•
Petrol Engines Diesel Engines Gas Engines
(4) Ignition Method :
•
•
Spark Ignition (SI) Compression Ignition (CI)

## Slide 9: Classification of IC Engines
(5) Cooling System:
Air cooled Engines
Water Cooled Engines
(6) Valves Location :
L head (Side valve) engine
T Head (Side valve) engine
I head (over head valve) engine
F head (over head inlet and side exhaust) engine

## Slide 10: I.C ENGINE TERMINOLGOGY
The standard terms used in I.C Engines are
Bore: Inside diameter of the cylinder is termed as Bore.
Top Dead Center (TDC): The extreme position reached by the piston at the top of the cylinder in the vertical engine is called Top Dead center.
Bottom Dead Center (BDC): The extreme position reached by the piston at the Bottom of the cylinder in the vertical engine is called Bottom Dead center.

## Slide 11: I.C ENGINE TERMINOLGOGY
9
Stroke: The nominal distance travelled by the piston in the cylinder between the extreme upper and lower positions of the piston (TDC &BDC) is termed as stroke.
Compression ratio (r): It is the ratio of Maximum cylinder volume to the Clearance volume.
Cylinder volume (v): It is the sum of swept volume and the Clearance volume.
V = Vs + Vc

## Slide 12: I.C ENGINE TERMINOLGOGY
Swept volume (Vs): It is the volume of space generated by the movement of piston from one dead center to another dead center.
Clearance Volume( Vc): It is the space in the cylinder, when the piston is at Top Dead Center
10

## Slide 13
61
Comparison between Four stroke cycle and two stroke cycle engine
(Merits and Demerits)
S.No.
Four Stroke Cycle Engine
1
2
Demerits: One power stroke in two revolutions of the crank shaft
Power developed for the same engine speed is theoretically half that of two stroke engine.
3
Two Stroke Cycle Engine
Merits: One power stroke in one revolution of the crankshaft
Power developed for the same engine speed theoretically twice that of a four stroke engine
Simple design and lighter in construction for the same power
For the same power complicated design and heavier in construction

## Slide 14
62
Comparison between Four stroke cycle and two stroke cycle engine
(Merits and Demerits)
S.No.
Four Stroke Cycle Engine
4
Two Stroke Cycle Engine
Merits:
Uniform torque is obtained. Hence a lighter fly wheel can be used
5
6
Design of ports is simpler. Hence initial cost is less
Mechanical efficiency is high. No moving parts like cam, follower, rocker
Demerits:
Non uniform torque on the crankshaft. Hence a heavier flywheel is required for balancing.
Design valve mechanism is difficult. Hence initial cost is more.
Mechanical efficiency is less. Power is lost due to friction caused by valve mechanism

## Slide 15
63
Comparison between Four stroke cycle and two stroke cycle engine
(Merits and Demerits)
S.No.
Four Stroke Cycle Engine
7
Two Stroke Cycle Engine
Merits: Starting is easy
Demerits: Starting is not so easy
8
These engines are generally air cooled
These engines are generally water cooled.

## Slide 16: Comparison between Four stroke cycle and two stroke cycle engine (Merits and Demerits)
64
2
S.No Two Stroke Cycle
. Engine
1 DeMerits:
Consumption of lubricating oil is more, because less time is available to remove the heat
More wear and tear of moving parts.
3
Some of the fresh air fuel mixture may escape with exhaust gases. Hence fuel consumption is more
Four Stroke Cycle Engine
Merits:
Consumption of lubricating oil is less, because more time is allowed for removing heat from the cylinder.
Less wear and tear of parts is less
Fuel cannot escape with exhaust gases. Hence fuel consumption is less.

## Slide 17: Comparison between Four stroke cycle and two stroke cycle engine (Merits and Demerits)
65
S.No Two Stroke Cycle
. Engine
4 DeMerits:
Thermal efficiency is less.
5
6
It produces more noise due to sudden release of exhaust gases
Scavenging is poor, since exhaust port is open only for a short time
Four Stroke Cycle Engine
Merits:
Thermal efficiency is more.
Noise is less is less. Exhaust gases are released in separate stroke.
Scavenging is better, since there is a separate exhaust stroke for the removal of exhaust gases

## Slide 18
66
Comparison between Four stroke cycle and two stroke cycle engine
(Merits and Demerits)
S.No.
Four Stroke Cycle Engine
7
Two Stroke Cycle Engine
DeMerits:
Poor scavenging leads to mixing of fresh charge with exhaust gases. This results in poor performance, slow running
Merits:
Better performance and efficiency is more
8
Used in light vehicles, like bikes, scooters, mopeds, etc.,
Used in heavy vehicles, like buses, lorries, trucks etc.,

## Slide 20
COMPONENTS OF AN I.C.
ENGINE
20

## Slide 21
21

## Slide 22: Cylinder Block
22

## Slide 23
Cylinder block is a basic structure of the engine on that other parts are involved.
Block contain Bore ,piston ,gasket ,pumps and other
components are attached to it.
It is made from the material aluminium alloyed, Grey cast iron, white iron, Grey iron.
4

## Slide 24
A cylinder is the central working part of reciprocating engine, the space in which a piston travels.
Cylinders may be sleeved (lined with a harder metal)
or sleeveless (with a wear-resistant coating such as Nikasil). A sleeveless engine may also be referred to as a "parent-bore engine".
Cylinder also consist of Inlets for the coolant to keep them cool during the combustion process.
5
Cycles inside the cylinder

## Slide 25: According to the cylinder arrangement in the engine it is classified as follows :
Fig.4 Types of cylinder arrangement
Source: www.google.com_search_cylinder arrangement
25

## Slide 26: Cylinder Head
26

## Slide 27
8
Cylinder Head
Cylinder Head diagram

## Slide 28
In an IC engine, the cylinder head sits above the cylinders. It closes in the top of the cylinder.
This joint is sealed by a head gasket to avoid the leakaging of gases.
In most engines, the head also provides space for the passages that feed air and fuel to the cylinder, and that allow the exhaust to escape.
The head can also be a place to mount the valves ,spark plugs, Studs, Bushes and fuel injectors.

## Slide 29: Spark plug

## Slide 30
The Spark plug supplies the spark that ignites the air/fuel mixture so that combustion can occur.
Spark plugs usually require voltage of 12,000–25,000 volts or more to "fire" properly, although it can go up to 45,000 volts. They supply higher current during the discharge process, resulting in a hotter and longer- duration spark.
Spark plug
Video:
How Spark Plug Works - Magic Marks.mp4

## Slide 31: Types of Spark Plugs
The classification is based on the operating temperature at the tip of electrodes as follows :
A. Hot Spark Plug
Short and thick centre electrode and insulator
The spark plug will heat up easily and reach its optimal operating temperature.
A. Cold Spark plug
The long and thin exposed electrode.
The plug that doesn’t reach a high temperature is a cold plug.

## Slide 32: What happens when a plug is too cold?
If the nose of the plug is not hot enough, it will gradually accumulate deposits, known as fouling.
During normal engine operation, residue from the combustion process hits the insulator nose.
If the insulator nose and electrodes are hot enough, the combustion deposits on the electrode.
Hence at too cold condition, the efficiency of the spark plug
decreases.

## Slide 33: What happens when spark plug is too hot?
When a spark plug gets too hot, the insulator may boil and bubble On examination, it will be plain that it has been too hot.
A too-hot plug that fails to destroy itself is when it destroys the engine instead; this is called pre-ignition.
If the tip of the plug becomes hot enough to ignite the fresh mixture being drawn into the cylinder, then the incoming mixture will start to burn without waiting for the spark to happen.
early ignition makes engines heat up, causing pre-ignition. Eventually, melting of the parts happens.
Hence at too hot condition, the efficiency of the spark plug decreases.

## Slide 34: Piston and Piston Ring

## Slide 35
16
piston with rings
Pistons are made up of aluminum alloy.
Piston slightly smaller than the cylinder which allows the piston to slide up and down that is in reciprocating motion this is sliding fit.

## Slide 36
It compress the fuel during compression stroke, and transmit power to the connecting rod.
The piston ring gives gas-tight fitting between piston and cylinder to prevent leakage of high pressure gasses.
The rings are split at one point. This allows them to be expanded slightly.
Upper two piston rings called compression rings, which seal between the piston and cylinder wall.
Lower piston ring is oil control rings.
17
piston rings
Video:
engine assembly working assembly of connecting rod piston assembly and crankshaft animation hd.mp4

## Slide 37: Connecting Rod

## Slide 38
As piston moves up and down, the rod journal moves in a circle and the crankshaft rotates.
As piston moves up and down, the connecting rod tilts back and forth.
This allows the big end of the connecting rod to follow the rod journal as it swings in a circle around the crankshaft.
The reciprocating motion of the crankshaft is changes in to rotary motion of the crankshaft.
Connecting Rod

## Slide 39: Fuel Injector

## Slide 40
The mixing of air and fuel depends on the induction swirl provided by directing the flow of air in desired direction through ports
Nozzle is the part of the injector through which fuel is injected to combustion chamber. There are single hole, multiple hole,pintle and pintaux types.
The actual mixing of air and fuel achieved by injecting fuel in the chamber through a nozzle under pressure more than 200 bar.

## Slide 41: Valves

## Slide 42
Most engines have two ports, one is intake port, other is
exhaust port.
When valve moves up in to its port, in this position valve is closed.
When valve is pushed down off its seat, the port is open.
Then the air fuel mixture can pass through the port.
The opening and closing of the valves are controlled by the valve train or Camshaft.
Cam Lobe

## Slide 43: Camshaft

## Slide 44
Camshaft decides the opening and the closing of the intake and
exhaust valves.
Cams are raised oval shaped section of a shaft that is called as
Lobes.
Lobes decides when valve will open.
As the camshaft rotates, the lobes rotates and push the valve open
Cam Lobe
25
or close.

## Slide 45: Camshaft can be either –
Overhead camshaft(OHC)
Camshaft is installed in the cylinder head.
Separate camshafts for the intake and exhaust valves
Overhead valve(OHV)
Valves are installed in the cylinder head
This arrangement requires valve lifter, push rod and rocker arms to transfer
camshaft rotation to valve movement
26
OHV
DOHC

## Slide 46: crankshaft
27

## Slide 47
the crankshaft.
Crankshaft
The crankshaft is an engine component that converts the reciprocating motion of the piston into rotary motion.
crankshaft includes the crankpin journal, throw, bearing journals, balance weights .
crankpin journal attach the connecting rod to
28

## Slide 48
The crank throw is the measurement from the centre of the crankshaft to the centre of the crankpin journal.
used to determine the stroke of an engine.
The longer the throw, the greater the stroke, or piston travels.
crank throw

## Slide 49: Flywheel

## Slide 50: efficiently store rotational energy.
A flywheel is a mechanical device specifically designed to
The piston moves by the pressure produce during combustion
,but the moves the piston only about half a stroke or one quarter of revolution of the crankshaft.
The flywheel stores some of the power produced by the engine.
The power is used to keep the piston in motion during rest of the four-stroke cycle.
Video:
How Flywheel Works_ - Magic Marks - YouTube (360p).mp4
Flywheel in the machine

## Slide 51: Timing Chain

## Slide 52
It synchronizes the rotation of the crankshaft and the camshaft(s) so that the engine's valves open and close at the proper time.
Higher torque engines that do a lot of heavy work, are usually equipped with timing chains. Trucks and heavy duty vehicles are usually equipped with timing chains to deliver more power.
Rubber timing belts are found in the majority of small cars and SUVs, particularly 4 cylinder engines that have lower torque.
Rubber timing belts are quieter and more efficient.
Timing gears are used to fix stretching or any other damage.
Video:
Timing Chain - YouTube (360p).mp4
Flywheel mechanism

## Slide 53
Any Questions ?

## Slide 54: Thank you